## Slide 7: Additional Slides
On flying turbocharged aircraft

## Slide 11: Mixture knob response to turbocharger failure

## Slide 15: From T206H POH

## Slide 16: From T206H POH

## Slide 18: Additional Concerns To Have in Mind
Higher operating temperatures require constant monitoring of CHT, EGT and TIT
Leaning increases the CHT, EGT and TIT significantly and rapidly.
Shock cooling and proper descent planning
Allow for cool down after landing. Engine oil lubricates the turbine and impeller. Refer to the engine's operator manual (see syllabus)
Weight and Balance: 200- 250 lbs heavier
Improper starting procedures and engine fires
Turbocharger failures and loss of engine power at rich mixture setting

## Slide 19: Additional Concerns (2)
Manual Wastegate (found in retrofits) – Overboost
Oil-pressure closes the wastegate Low oil-pressure and cold oil prevents wastegate to open and the engine from developing full take off power
Engine oil lubricates the turbine spinning at 30,000rpm at take off.
Apply power smoothly and slowly to prevent surge and overboost
100 octane required because of higher operating temperatures, lower octane causes detonation.
Long taxi watch temperatures
Run up and hold short, turn into wind